|  | International Stoneworks 2523 Fairway Park Dr # 510 Houston, TX 77092 USA 1-(713) 956-8291 | PRODUCT DATA SHEET SEAL & GO® W |
| --- | --- | --- |

Seal & Go® W 					WATER-BASED PREMIUM IMPREGNATOR

Note:	To insure product performance and satisfaction, Always pre-test this product in an

inconspicuous area. User must determine suitability of product for their intended use.

Before applying sealer/impregnator, make sure all surfaces to be treated are thoroughly clean and completely dried.

      Apply and saturate all surfaces with Seal & Go® W allowing it to puddle and completely saturate the entire surface.  Seal & Go® W can be applied with a paint brush, paint roller, paint pad/applicator, clean towel or low pressure sprayer with no more than 25 psi.  Note: Do NOT Aerosolize.

      Allow Seal & Go® W to absorb and penetrate the entire

surface 15-30 minutes. Wipe up any excess by wiping the surface with a clean towel.

      Allow a minimum of 30-40 minutes drying time.

      Apply a second coat of Seal & Go® W to the entire

surface allowing it to penetrate and absorb. Make sure all surfaces are evenly coated.

Some areas may absorb more quickly than others. Let sit 15 minutes and wipe up excess

with a clean dry towel.

     Allow 24 hours for Seal & Go® W to completely dry and

cure for best results.

COVERAGE	    	Application rates for natural stone, tile, grout and masonry will vary depending on the 				porosity of the substrate to be treated. Some stone and grout areas will absorb more quickly 			than other areas.

Approximate Coverage Per Coat

Low Porosity               800-1000   sq. ft./gallon

Medium Porosity         400-800     sq. ft/gallon

High Porosity               100-400     sq. ft/gallon

Note: Less impregnator will be needed when applying a second coat.

Re-apply Seal & Go® W every 2-5 years or as needed basis depending

on area usage.

MAINTENANCE	Natural stone needs to be cared for properly. Seal & Go® W is not

an absolute barrier to all spills, stains and soils, however natural stone, tile, grout and

masonry will repel stains and soils effectively when proper cleaning products and methods

are used. This application does not eliminate the need for routine cleaning and maintenance.

International Stoneworks makes a full range of products for stone protection and

maintenance.

SAFETY

PRECUATIONS		KEEP OUT OF REACH OF CHILDREN.

	Protect and cover surfaces not to be treated by this product.

- Do not use this product with high pressure sprayers. Use low pressure sprayers with no more than 25 psi. Do not Aerosolize.

- Do not breathe spray or mist. Use this product with adequate ventilation.

- Use only as directed. Wear protective gloves and goggles when using. Avoid eye and skin contact. Do not breathe mists or spray. Keep container closed when not in use.

TECHNICAL		For additional technical support, contact International Stoneworks at 1-(713) 956-8291

SUPPORT		 Monday – Friday from 8:30am-5:00pm CST.

The information contained herein is based upon practical experience with Seal & Go® W. It does not constitute a guarantee. Purchasers shall determine the suitability of such products for their own purposes. User assumes all risks and liability whatsoever in connection therein. Manufacturer shall not be liable for any injury or inability to use this product.

# Text boxes

TYPICAL

APPLICATIONS

ADVANTAGES

DESCRIPTION    Seal & Go® W  is a water-based VOC compliant impregnator that  provides maximum protection for all  interior/exterior natural stone, marble, granite, limestone, brick, slate, saltillo, unglazed tile, grout and masonry surfaces while preserving its natural appearance. Seal & Go® W is not a surface coating but forms a vapor permeable barrier that resists stains and makes cleaning easier.

Superior Stain Resistance			VOC Compliant in All 50 States

Deep Penetrating Protection			Interior and Exterior Use

Preserves Natural Appearance		Inhibits Efflorescence

Excellent Oil and Water Barrier		Water-Based/Non-Flammable

Vapor Permeable (Breathable)		Non-Yellowing/U.V. Resistant